## Slide 1: Notes for Importing and Exporting GDS Files
RFVLSI LAB

## Slide 2: Layer Map Consistency
Before exporting and importing GDS files, one should check the tsmcN65.layermap file
All the Layer Stream Number and the Datatype Stream Number of your own layermap file should be consistent with RFVLSI Lab’s layermap file
File directory: /home/PDKs/OA65_LIB/tsmcN65/tsmcN65.layermap

## Slide 3: Import a GDS File
From CIW
  File -> Import -> Stream …
  At “Stream File”, choose your GDS file
  At “Library”, choose the importing destination library (Create this library before you import your GDS file)
  At “Attach Technology Library”, choose tsmcN65
  Click “Apply”, and the importing procedure will begin

## Slide 4: Export a GDS File
From CIW
  File -> Export -> Stream …
  At “Stream File”, name your GDS file
  At “Technology Library”, choose tsmcN65
  At “Library”, fill in the library name which contains your layout cell view
  At “Top Level Cell(s)”, fill in the top cell name of your layout
  At “View(s)”, fill in your cell view name of your layout
  Click “Apply”, and the importing procedure will begin

## Slide 5: Important Notes
When you are integrating the designs from other people, make sure that all the designers have checked and confirmed the correctness of their own designs by themselves
After all the designer have no problem with the imported layouts from their GDS files, you leave all the responsibility to them
If there are problems regarding to their chips after taping out, they should be responsible to themselves