## Slide 1: RFVLSI Dummy Layer Usage Guide
Yu-Jiu Wang

## Slide 2: Device Layers
Layer | Purpose | Usages
RFVLSI | Drawing | Device layers with device mainly in active, poly,…etc. layers. (Note, layers below M1)
RFVLSI | Dummy1 | Device layer with device mainly in M1.
RFVLSI | Dummy2 | Device layer with device mainly in M2.
RFVLSI | Dummy3 | Device layer with device mainly in M3.
RFVLSI | Dummy4 | Device layer with device mainly in M4.
RFVLSI | Dummy5 | Device layer with device mainly in M5.
RFVLSI | Dummy6 | Device layer with device mainly in M6.
RFVLSI | Dummy7 | Device layer with device mainly in M7.
RFVLSI | dummy8 | Device layer with device mainly in M8.
RFVLSI | Dummy9 | Device layer with device mainly in M9.
* When defining a device using above layers, it must come with a recognition TEXT in the same dummy layer.

## Slide 3: Pin Layers
Layer | Purpose | Usages
RFVLSI_PIN | Drawing | Pin layers in poly.
RFVLSI_PIN | Dummy1 | Pin layer with device mainly in M1.
RFVLSI_PIN | Dummy2 | Pin layer with device mainly in M2.
RFVLSI_PIN | Dummy3 | Pin layer with device mainly in M3.
RFVLSI_PIN | Dummy4 | Pin layer with device mainly in M4.
RFVLSI_PIN | Dummy5 | Pin layer with device mainly in M5.
RFVLSI_PIN | Dummy6 | Pin layer with device mainly in M6.
RFVLSI_PIN | Dummy7 | Pin layer with device mainly in M7.
RFVLSI_PIN | dummy8 | Pin layer with device mainly in M8.
RFVLSI_PIN | Dummy9 | Pin layer with device mainly in M9.
When defining a pin using above layers, it must come with a recognition TEXT in the same dummy layer.
Note, GDS streaming number 301 is used for 209-255 in the “T-N65-CL-LE-001” is conflicts with virtuoso system reserved layer.

## Slide 4: LVS metal removal layers
Layer | Purpose | Usages
RFVLSI_LVS | Drawing | Poly removal for connection extraction.
RFVLSI_LVS | Dummy1 | M1 removal for connection extraction.
RFVLSI_LVS | Dummy2 | M2 removal for connection extraction.
RFVLSI_LVS | Dummy3 | M3 removal for connection extraction.
RFVLSI_LVS | Dummy4 | M4 removal for connection extraction.
RFVLSI_LVS | Dummy5 | M5 removal for connection extraction.
RFVLSI_LVS | Dummy6 | M6 removal for connection extraction.
RFVLSI_LVS | Dummy7 | M7 removal for connection extraction.
RFVLSI_LVS | dummy8 | M8 removal for connection extraction.
RFVLSI_LVS | Dummy9 | M9 removal for connection extraction.
No text labels are required, for LVS metal removals.
Note, GDS streaming number 300 is used for 209-255 in the “T-N65-CL-LE-001” is conflicts with virtuoso system reserved layer.

## Slide 5: DRC Support for Erroneous Short Circuit
To find the above two type of errors. A DRC check needs to be implemented!

## Slide 6: DRC rules to find erroneous short!
Use Area B to find overlap with erroneous VIAS!!
Use Area C to find overlap with erroneous metal Short!!

## Slide 7: Layout editor priorioties
techLayerPurposePriorities( ;layers are ordered from lowest to highest priority ;( LayerName Purpose ) ;( --------- ------- ) ( PO drawing ) ( CO drawing ) ( CO2 drawing ) ( M1 drawing ) ( VIA1 drawing ) ( M2 drawing ) ( VIA2 drawing ) ( M3 drawing ) ( VIA3 drawing ) ( M4 drawing ) ( VIA4 drawing ) ( M5 drawing ) ( VIA5 drawing ) ( M6 drawing ) ( VIA6 drawing ) ( M7 drawing ) ( VIA7 drawing ) ( M8 drawing ) ( VIA8 drawing ) ( M9 drawing ) ( CB drawing ) ( CB2 drawing ) ( AP drawing)

## Slide 8: Layout rules changing procedure guide line.
Always dump the latest tech file including all layers.
Check TSMC layer TSMC GDS Layer Usage Description.
  Choose suitable layer.
  Note, layer 204-??? is system reserved.
  In tsmcN65, we choose 300, 301 for RFVLSI_PIN, RFVLSI_LVS dummy layers.
Change ./tsmcN65 to 777 before changing tech file.
Load the modified technology file.
Change ./tsmcN65 back to 755 after updating tech file.