## Slide 1: NCTU IEE 5046 高頻電路設計與實驗 Allegro PCB Editor - Create Package Symbol
Lecturer: Professor Yu-Jiu Wang
TA: 李道一michael@rfvlsi.ee.nctu.edu.tw
Document coauthor: Jon-Jin Chen

## Slide 2: Package Symbol
Two category of footprints:
  SMT – Surface Mount Technology
  TH – Through Hole
Surface Mount Technology
Through Hole

## Slide 3: New Package Symbol
Menu -> File -> New
Remember to save package symbol at $psmpath

## Slide 4: Basic Environment Setup
Menu-> Setup -> Design Parameters
Grid
  Turn on
  1 mil
Units
  Use English units (mil) to avoid conversion errors

## Slide 5: Look For Datasheet
Digikey
  http://www.digikey.com
Mouser
  http://www.mouser.com
Extract Dimensions
  Use professional version of Adobe Acrobat
  Use Autocad
  By hand

## Slide 6: Through Hole Example
Using: Murata PV 37 Series
Be careful of the units
Define pin numbers as datasheet suggests

## Slide 7: Through Hole Example
Steps:
  Define Origin
    Center of n-th pin
    Package Edge
    Change origin dynamically for convenience
  Write down dimensions on a draft paper first
  Prepare pad-stack with pad designer
    Configure drill holes on pad-stack
  Place Pads

## Slide 8: Place Pins for a Symbol
把Pin放到Package上
Layout -> Pins
從右邊的option選擇要用的Padstack
Manually assign coordinate for accuracy
  P : Pick Point
  A : Toggle Absolute /Relative Mode

## Slide 9: Modify Pins After Placement
還有Rotation的角度(選完後再按一次 Layout -> Pins)
  Use context menu to move, than use context menu again to rotate
還有最重要的Pin #
  要和capture上的腳位一模一樣
  Use Edit text to change Pin #

## Slide 10: Assign Reference Designator (RefDes)
設定Device Type和Ref Des
Add -> Text (任意字串e.g. J*)
在右邊Option選擇Device Type/ Silkscreen_Top放在第一個pin

## Slide 11: Assign Package Boundaries
選擇Setup -> Areas -> Package Boudarys 後,選矩形 把整個元件包起來(Pin的部分)

## Slide 12: Create Device File and Symbol (*.psm)
存檔: File -> Save
製作元件: File -> Create Device